## Slide 1: Avian Hazard Advisory System (AHAS) Training Presentation
Current as of 2 Oct 2012

## Slide 2: OBJECTIVE
Introduce users to the AHAS system by highlighting specific capabilities, common pitfalls, and best practices
Objective

## Slide 3: OVERVIEW
Background
Outputs
Current Conditions (current hour query)
Forecast Conditions (1 < x ≤ 24 hrs query)
Historical Conditions (> 24 hr query)
Common Pitfalls
Best Practices
Overview

## Slide 4: BACKGROUND
Predicts bird movements within low level flight arena for the contiguous 48 states and Alaska
Found at http://www.usahas.com
Uses filtered NEXRAD data, National Weather Service (NWS) Forecasts, Migratory Bird and Soaring Bird Forecast Models, and Bird Avoidance Model (BAM) to predict bird movements
Provides CONUS and Alaska bird strike risk for:
  IR, VR, and SR routes
  Ranges and MOA’s
  Military and Civilian Airfields
  Alert Areas
Background

## Slide 5: BACKGROUND
If you request information for:
  Current Hour: risk is based on observations made by the NEXRAD weather radar system, or data from the Migration & Soaring Models
  Less Than 24 hrs (1 < x ≤ 24 hrs query): risk is based on the Migration & Soaring Models (with imbedded NWS data) or the US BAM. These models forecast conditions favorable for hazardous bird activity to be present
  More Than 24 hrs, or historical (> 24 hour query or past conditions): risk information comes from the current version of the US BAM
Background

## Slide 6: AHAS CENTRAL QUERY PAGE
AHAS immediately directs you to the query page. Check for news and other important information using the tabs at the top
AHAS now allows you to select airfields based on the ICAO
To request a unit specific page, contact the USAF BASH Team
You can also select output type
Select output as a table, map, or with Google Earth
AHAS web page tabs
Background

## Slide 7: Table Output
Search Criteria: VR 086 (1, 2), current hour in Zulu (3), output choice (4)
AHAS indicates the driving model (5) for the overall risk (6)
The results from NEXRAD will always be shown for the current hour(7)
AHAS also shows the nearest five other routes(8)
AHAS now shows hazards found along the route(9)
Data auto updates every 6-10 minutes
5
4
3
2
1
6
Outputs
7
9
8

## Slide 8: 12 Hr Table Output
Search Criteria: VR 086 (1, 2), hour in Zulu (3), output choice (4)
AHAS indicates the driving model (5) for the overall risk (6)
NEXRAD risk is only available for the current hour
12 hours of risk will be shown starting at the selected hour
Scroll down for more hours (7)
No hazards or alternate routes are shown on the 12 hour web page
Expect longer download times for expanded data
5
4
3
2
1
6
Outputs
7

## Slide 9: Table Output Risk determination
The AHAS risk is determined based on the highest risk between the soaring model and the NEXRAD risk
If both the NEXRAD risk and the soaring data are not available, the AHAS risk will be based on the BAM
  If the NEXAD risk is missing and the soaring model is LOW, the AHAS risk will be based on the BAM
  If the soaring data is missing and the NEXRAD risk is LOW, the AHAS risk will be based on the BAM
Missing NEXRAD data will be indicated on the web page as “NO DATA” in the NEXRAD column
Missing soaring data will be indicated on the web page as “NO DATA” in the Height column
Outputs

## Slide 10: MAP OUTPUT
Search Criteria: VR 1305, selected route highlighted in blue
Map Output is not available for unit- specific pages or Alert Areas
If you select this output, data will default to BAM readings
May select different mapping features within BAM
Default BAM underlay is current biweek, day period
Includes mapping tools: zoom, pan, full extent, back extent, forward extent, identify, measure and overview map
Outputs
Moderate risk
Low risk
Severe risk

## Slide 11: GOOGLE EARTH OUTPUT (available only on Google Earth enabled computers)
Search Criteria: VR 086, current hour
Risk matches table results and auto updates every 6-10 minutes
Hazards can be turned on or off (1), ON in this image
BAM layers can be turned on or off (2), OFF in this image
Route segment color defines warning level
Green = Low
Yellow = Moderate
Red = Severe
Outputs
1
2

## Slide 12: CURRENT HOUR QUERY
Current Condition Query
  Uses NEXRAD weather radar system (updated every 6-10 minutes) to monitor large-scale migratory bird activity in the CONUS and Alaska
  Includes risk from migration and soaring bird activity
  Risk displayed defaults to the most severe prediction model (NEXRAD, Migration, or Soaring)
    Displayed thermal depth height offers maximum altitude and below where conditions are optimal for hazardous soaring birds to be present
    May use BAM data if no other inputs are available
  “Based On” field indicates primary source of risk
Queries

## Slide 13: CURRENT HOUR QUERY Calculating NEXRAD risk
AHAS uses two factors to calculate NEXRAD risk: “Severity” is based on the dBZ (decibels of Z, where Z represents the energy reflected back to the radar) and “Probability” of a bird strike (percentage of area polygon filled with reflectable biological activity)
AHAS calculates NEXRAD risk by multiplying Severity and Probability to get a value in the below table (Green = Low, Yellow = Moderate, and Red = Severe)
 | Probability |  |  |  | 
Severity(z) | 20 | 40 | 60 | 80 | 100
3 | 60 | 120 | 180 | 240 | 300
10 | 200 | 400 | 600 | 800 | 1000
30 | 600 | 1200 | 1800 | 2400 | 3000
100 | 2000 | 4000 | 6000 | 8000 | 10000
300 | 6000 | 12000 | 18000 | 24000 | 30000
Queries

## Slide 14: CURRENT HOUR QUERY
Query Example – A P HILL AAF
  Go to www.usahas.com
  Click desired area (1, Airfields)
  Select A P HILL(2), current hour in Zulu (3), and output format (4)
  Note: Airfield Category predicts conditions around and above airfields and not on the fields themselves
  Actual airfield conditions should be determined by observed conditions and relayed through BWC
2
1
3
4
Queries

## Slide 15: CURRENT HOUR QUERY
Hazards
Date time of risk
Defines which model/input is driving the risk reading; in this case, NEXRAD Model
Thermal depth: indicates max altitude (AGL) where soaring birds might be present. In this case, “NA” indicates that the risk is not based on the soaring model. “NO DATA” indicates that the soaring data is missing
Overall AHAS risk driven by highest risk model; NEXRAD model overrides any ties
Queries
NEXRAD risk:
“NO DATA” indicates that the radar is down

## Slide 16: FORECAST QUERY (>1 and up to 24 hours)
Forecast Conditions Query
  NWS weather observations and forecast model data predict large-scale migratory and soaring bird activity in the contiguous 48 states and Alaska
  Migratory and Soaring models are run twice a day to forecast bird strike risk up to 24 hours in advance
  The Migratory Bird Forecast Model predicts likelihood of migration of known concentrations of large birds, given current and forecast weather conditions
  The Soaring Bird Forecast Model predicts likelihood of soaring birds based on calculating thermal depth and US BAM data
    Displayed thermal depth height indicates where conditions are right for soaring birds to be present
Queries

## Slide 17: FORECAST QUERY (>1 and up to 24 hours)
Query Example – AP Hill
  Go to www.usahas.com
  Click desired area (Airfields)
  Select AP Hill, desired time, and select output format
  Everything is the same as a current hour query except you select a time between 1 and 24 hrs from current time
Next hour selected
Queries

## Slide 18: FORECAST QUERY (>1 and up to 24 hours)
Query is from between 1 and 24 hours of the current time
Outside of 1 hour NEXRAD data is not available.
Defines which model/input is driving the risk reading. In this case, SOAR Model
Queries
Thermal depth: indicates max altitude (AGL) where soaring birds might be present. In this case, “33” indicates that conditions are right for soaring birds to be present at 3,300’ AGL and below

## Slide 19: HISTORICAL QUERY (>24 hrs or the past)
AHAS risk prediction reverts to the BAM if:
  Query is for any time prior to the current hour
  Query is for time period >24 hrs in advance of the current hour
  Other data sources are unavailable
Past data can be requested from the USAF BASH Team
Queries

## Slide 20: HISTORICAL QUERY (>24 hrs or the past)
Bird Avoidance Model (BAM) data is based on:
  All bird species present during a particular daily time period, in a particular area, for one of 26 two-week periods in a year
  Geographic information for observations of 60 key BASH species, over a 30-year period
  Several key datasets, including the Audubon Society’s Christmas Bird Count (CBC), the US Biological Survey's Breeding Bird Survey (BBS), bird refuge arrival and departure data for the conterminous US, and data specific to a particular bird species
  Common behavior of species groups modeled for dawn, day, dusk, and night
Queries

## Slide 21: COMMON PITFALLS
Misperception: historical data from AHAS contains forecasted or current hour data
  Requested historical data is from the US BAM only
Using AHAS to determine Bird Watch Condition code
  AHAS is not precise enough for use within airfield boundaries
Expecting NEXRAD data for forecasted and historical queries
  NEXRAD is updated every 6-10 minutes for current hour queries only and can not be forecasted or give historical data at this time
Pitfalls

## Slide 22: BEST PRACTICES
Use BAM data when acquiring route times
  Adjust/modify routes based on AHAS forecasts
Use BAM in conjunction with AHAS during planning
  Pinpoint wildlife attractants along route of flight
  Identify NEXRAD coverage areas or nearest radar to route
Access AHAS just prior to step time
Incorporate ops procedures in local BASH plan
  Call SOF/Sqdn Ops to get current AHAS reading prior to base departure, low-level segments, or when approaching airfield/training area
Utilize Unit Specific AHAS Web Pages
Best Practices

## Slide 23: BEST PRACTICES (Unit Web Pages)
Unit Web Pages can include:
  Transition bases
  Flight routes
  Ops and Range Areas
  Specific data impacting mission
Unit Web Pages are ideal for:
  Operations Supervisors
  SOFs
  Crews stepping to fly
Unit Web Pages can be tailored to suit user’s needs
Hazards do not display on unit web pages
Best Practices

## Slide 24: CONTACT INFORMATION
USAF BASH Team
  Mr. Dan Sullivan, Branch Chief daniel.sullivan@kirtland.af.mil, DSN 246-5674
  Mr. Ted Wilkens, Programs and Initiatives ted.wilkens@kirtland.af.mil, DSN 246-5673
  Lt Tiffany Robertson, Wildlife Ecologist tiffany.robertson@kirtland.af.mil, DSN 246-5848
  Commercial prefix is (505) 846-xxxx
AHAS Personnel
  Mr. Ron White
  ahas@detect-inc.com
Contact Info